| VoIP Qualification Checklist This Qualification sheet is designed to help you understand and check that your technical environment is set up and meets the minimum requirements for the VoIP service to work for your business. Please make sure that you familiarise yourself with these requirements before you initiate the ordering of the VoIP service. |
| --- |
| Section 1: Customer Business Details |
| Business Name: |  | ACN/ABN |
| Address: |  | Fax No: | Tel No: |
| Case Ref: |  |  |
| Contact Name: |  | Email: |
| Contact Mobile Number: |  | Tel No. |
| Section 2: VoIP Minimum Network Requirements 2.1 Do you have a broadband internet connection with a minimum of 100 kbps allocated for every concurrent voice session? YES NO 2.2 Is your network capable of providing DHCP, and DNS Service? YES NO 2.3 Do you have enough power outlets or / PoE ports available at each location (All VoIP handsets are delivered with a power supply)? YES NO 2.4 Do you have enough LAN switch port capacity, and the required cabling and patching in place? 2.5 Do you have a plan on how to manage your existing voice related PSTN services, if any (e.g. fax, EFTPOS, HICAPS, Back-To-Base Security alarm services, etc…)? YES NO YES NO |
| Section 3: Firewall Requirement 3.1 Disable SIP-ALG (Application Layer Gateway) YES NO 3.2 Firewall open for outbound connections as per table below YES NO Destination IP Addresses Protocol Port Number Description 203.63.96.24 TCP 80, 443 Web Access and SSL 203.63.96.25 TCP 80, 443 Web Access and SSL 203.63.96.26 TCP 80, 443 Web Access and SSL 203.63.96.27 TCP 80, 443 Web Access and SSL 203.63.96.28 TCP 80, 443 Web Access and SSL 203.185.248.15 TCP/UDP 5060 SIP Signalling 202.92.115.50 TCP/UDP 5060 SIP Signalling 203.185.248.15 UDP 60000-65535 RTP Media 202.92.115.50 UDP 60000-65535 RTP Media 203.63.96.15 UDP 123 NTP Server |
| Section 4: LAN/WAN Connectivity test 4.1 Performed VoIP Connection test successfully, and have captured test results and test numbers YES NO Tool works best with Mozilla Firefox browser with Java enabled. URL: http://myconnectionserver.aapt.com.au/myspeed/VoIPconnectiontest MySpeed Test Number : MyVoip Test Number : |
| Section 5: Receptionist Console Requirements (If applicable) These are the minimum hardware and Software requirements for the Receptionist application Console. 5.1 Windows XP with SP3 (or higher), Windows Vista, Windows 7, Windows 8, Mac OS X 10.5 or 10.6, or Citrix XenApp 4 or 5 YES NO 5.2 Internet Explorer 8.0, 9.0 or 10.0; Firefox 17 or later; Google Chrome 17.0.963.64 or later; or Safari 5 or 6 YES NO |
| Section 6: UC One Desktop Software Client Requirements (If applicable) These are the minimum hardware and Software requirements for the VoIP Desktop application. 6.1 Mac OS 10.8 Mountain Lion, Mac OS 10.9 Mavericks, Mac OS 10.10 Yosemite, Windows Vista, Windows 7 or Windows 8/8.1 or Windows 10 (Classical view only) YES NO 6.2 Minimum 1.5 GHz CPU, Pentium 4, dual core CPU with 2GB RAM YES NO 6.3 The installation footprint is approximately 125 megabytes (MB) on OS X and 215 MB on Windows YES NO 6.4 For voice calls, a sound card, speakers, and a microphone or a headset are required YES NO |